Author:          Lauge Fuglsang Nielsen

Title:			“Time-dependent behaviour of concrete - a basic algorithm for FEM-analysis'

Presentation:  Bygningsstatiske Meddelelser, LXX(1999), 51-83.

A so-called incremental stress-strain model convenient for FEM-analysis of concrete structures is presented in this paper. Concrete composition is considered by the model as well as age at loading and curing conditions. No other incremental models presented in the literature offer these features in one approach. Only two sets of material constants have to be calibrated experimentally or chosen from experience.

The results of applying the method developed are successfully compared with experimental data reported in the concrete literature, such as data recently reported by the Technological Institute of Denmark (DTI) from tests on a typical high performance concrete. Furthermore the method is compared with other incremental methods, which assume concrete to be a homogeneous continuum. It is shown that the method developed in the paper is in general superior to such methods. It is additionally shown that the method developed can be used in stress analysis of concretes developing from ages as young as approximately half a day.

The program attached is a demonstration of how the algorithm works when the concrete considered is subjected to relative simple load- and curing histories. The program can easily be generalized to consider load and curing in general. In order not to loose transparency, however, it is chosen not to do so.

Basic references:

The paper presented above is based on a complete composite stress-strain analysis of concretes of ages down to 12 hours. This analysis is reported in:

“Composite analysis of concrete - Creep, relaxation, and eigenstrain/stress”, Report 112(1997), Ministry of Transport, Road Directorate, Denmark, (Part of a major research project, “HETEK, Control of early age cracking in concrete”).

"ComCon - Software for Composite analysis of concrete (Creep, relaxation, eigenstrain/stress, loss of prestress): Underlying theory and documentation", Report I 21(1999), Dept. Struct. Eng. and Materials, Tech. Univ. Denmark.

"ComCon - Software for Composite analysis of concrete (Creep, relaxation, eigenstrain/stress, loss of prestress): Users Manual", Report I 22(1999), Dept. Struct. Eng. and Materials, Tech. Univ. Denmark. (Co-author, Paw Mullit).