Author:          Lauge Fuglsang Nielsen

Title:              Generalized Bingham description of fresh concrete

Presentation:  XVIII Symposium on Nordic Concrete Research, 12-14 June 2002, Helsingør, Denmark, Proceedings Danish Concrete Society, 2002.

A method is presented by which the well-known Bingham description of flow in homogeneous liquids with yield stress can be generalised to apply also for composite fluids. In the present context such fluids are defined as traditional Bingham fluids mixed with very stiff particles of known shapes and size distributions. In practice the composite aspects of the generalised Bingham description is a major advantage. Only a few geometrical parameters for the particles and two material properties for the fluid matrix are required in order to describe the Bingham behaviour of any composition of the composite fluid considered. The Bingham method normally used needs experimental calibration for any new composition. In the paper composites thought of are self-compacting concretes (SCC) modelled as aggregates in a fluid matrix of cement paste (or mortar).

Related papers:

Nielsen, L. Fuglsang: "Rheology of some fluid extreme composites - such as fresh self-compacting concretes", Nordic Concrete Research, 2(2001), 83-93

Idem: "Rheology of extreme composites", Papers in Structural Engineering and Materials - a Centenary Celebration,  Struct. Eng. and Materials, Tech. Univ. Denmark, 2000.

# Software

A software, SCC, is developed which handles the somewhat complex expressions presented in the papers. The software covers the aggregate concentrations met in most normal concretes.

A special version of SCC, SCCVAN, is specially developed to consider low ‘aggregate’ concentrations as in fibre concrete.